WESTERN CONNECTICUT STATE UNIVERSITY

AEROSOL CAN MANAGEMENT PLAN

PROCEDURE  E-108

Issued 4/25/02

Revised 9/6/02; 11/5/03; 4/29/05; 3/1/06; 11/14/18, 5/28/2020

Please direct any questions or comments about the applicability of this document to

David Serino, Director of Environmental & Facilities Services

- PURPOSE

The purpose of this procedure it to establish policy on the accumulation, collection, and processing of aerosol cans and their contents.  According to the EPA, any can that did contain, or does contain, hazardous constituents that would be a “listed” or “characteristic” hazardous waste is subject to RCRA regulations unless the can is fully evacuated of its contents.

- SUMMARY OF APPLICATION

The State of Connecticut requires that all spent aerosol cans be collected and their contents managed in accordance with the Universal Waste Rule as adopted by the State of Connecticut (10/31/2000).  According to section 22a-449(c)-113, aerosol cans are referred to as “low risk, high volume hazardous wastes” and subject to regulation as universal waste.

- SUMMARY OF FUNCTION

A designee of the Director of Environmental & Facilities Services collects the aerosol cans monthly from designated accumulation sites. An approved Aerosol Evacuation Device is used to puncture and drain compatible aerosol cans.  The cans are sorted according to compatibility. Pesticide containing cans are lab packed separately.  Once the segregation has been made, the designee determines whether the aerosol cans are still operational.  If a can is still good, it will be recirculated for further use.  If the can, however, is spent, it will be punctured, emptied, and disposed of.  Using the Aerosolv device, the designee presses on a handle that causes a puncture pin to pierce the can, which is secured inside a cylinder.  The can’s contents are then collected in a drum and managed as hazardous waste.  Any aerosol can that is completely emptied (i.e., does not contain propellant or product and is at atmospheric pressure) is not regulated as hazardous waste, per 40 CFR 261.7, even if it contained hazardous substances.  Therefore, the evacuated cans will be placed into receptacles and recycled as scrap metal.

NOTE:  Only cans containing compatible materials will be disposed of using the above mentioned procedure.  All other cans will be lab packed.

- OPERATIONAL RULES

Authorized receptacles for aerosol cans (labeled 5-gallon buckets) are located in each building on the Midtown and Westside campuses. Cans can be accumulated at the designed areas until a determination is made regarding the operational status of each can.

Under no circumstances are aerosol cans allowed to accumulate or be stored outside of these labeled receptacles.  A pick up certification from (Appendix 1) will be completed in order to document frequency of pollutions.

The designated rooms for the accumulation of aerosol cans are as follows:

Midtown Campus				     Westside Campus

| Building | Room# |  | Building | Room# |
| --- | --- | --- | --- | --- |
| Berkshire Hall | 002 |  | Ella Grasso Hall | Main Valve Room |
| Fairfield Hall | Custodial Closet Across From 104 |  | O’Neill Center | Receiving (adjacent to gate 5) |
| Haas Library | Mechanical |  | WS Classroom Building | 124 (time clock) |
| Higgins Hall | Custodial Stoarge |  | A. Searle Pinney Hall | Loading Dock |
| Litchfield Hall | Mechanical Room |  | Centennial Hall | E034 Storage |
| Newbury Hall | Basement-Machine Room |  |  |  |
| Old Main | 021 Custodial Closet |  |  |  |
| Police Boiler House | Garage Garage |  |  |  |
| Student Center | 008 Storage |  |  |  |
| University Hall | Electrical Room |  |  |  |
| Warner Hall | Room Across From 113 |  |  |  |
| White Hall | Main Valve Room (inside 031 |  |  |  |

Science Building                105 – Recycling

## Custodial Responsibilities

The custodial staff is required to place all spent aerosol cans into authorized receptacles in the room designated for the building they are working in.

Appendix 1

Pick Up Certification

| Midtown Buildings |  |  |
| --- | --- | --- |
| Building | Room # | Date |
| Berkshire Hall | 002 (storage) |  |
| Fairfield Hall | 1st wing closet |  |
| Haas Library | Mechanical |  |
| Higgins Hall | Custodial Storage |  |
| Litchfield Hall | Mechanical Room |  |
| Newbury Hall | Basement-Machine Room |  |
| Old Main | 021(custodial storage) |  |
| Police | Garage |  |
| Boiler House | Garage |  |
| Student Center | 008 (storage) |  |
| University Hall | Electrical Room |  |
| Warner Hall | 112 |  |
| White Hall | Room 031 |  |
| West Side Buildings |  |  |
| Building | Room # | Date |
| O'Neill Center |  |  |
| Classroom Building | 124 (time clock) |  |
| A. Searle Pinney Hall | Loading Dock |  |
| Ella Grasso Hall | Main Valve Room |  |
| Centennial Hall | Room E034 |  |

University Certification

Procedure E-108 (Aerosol Can Management Plan), for the Western Connecticut State University campus located in Danbury, Connecticut, has been reviewed and approved by the appropriate personnel at Western Connecticut State University.  The procedures in this plan will be implemented and amended, as necessary, due to expansions, modifications, and improvements at the campus.

Signature: 		Date: 5/28/2020

Luigi Marcone

Chief Facilities Officer & Associate Vice President for Campus Planning

Telephone Number: (203) 837-9314

Western Connecticut State University

181 White Street

Danbury, Connecticut 06810