## Slide 1
Presenter: Sanja Perica, Ph.D.
Chief, Hydrometeorological Design Studies Center (HDSC),
Office of Water Prediction, National Weather Service, NOAA
Email: Sanja.perica@noaa.gov
Web: www.nws.noaa.gov/oh/hdsc
Authors: Sandra Pavlovic, Sanja Perica, Michael St Laurent, Carl Trypaluk,
Dale Unruh, Orlan Wilhite
Weather Conference
Western Connecticut State University, Danbury, CT
29 September 2018
Evaluating Impacts of Recent Major Storms and Non-Stationary Climate Conditions on
NOAA Atlas 14 Precipitation Frequency Estimates

## Slide 2
    HDSC
    part of the NOAA/National Weather Service's Office of Water Prediction http://www.nws.noaa.gov/ohd/hdsc/
    Responsibility: preparing national standards and updating Precipitation Frequency (PF) estimates for various parts of the USA and affiliated territories.
About HDSC and NOAA Atlas 14
NOAA Atlas 14
Since 2004, updates are published as Volumes of NOAA Atlas 14
S. Perica, NOAA/NWS/HDSC Weather Conference, Danbury, 29 September 2018 2

## Slide 3
Variety of infrastructure design and planning activities under federal, state, and local regulations
    Storm water drainage
    FEMA’s National Flood Ins. Program
    Water-quality management
    Etc.
For monitoring observed and forecasted precipitation to indicate flooding threats
Estimating severity of historic events
S. Perica, NOAA/NWS/HDSC Weather Conference, Danbury, 29 September 2018 3
Applications
Design criteria.
Frequency analysis of Hurricane Harvey.

## Slide 4
  30 arc-sec PF grids with confidence limits in GIS format for 5-min to 60-day; 1- to 1,000-year ARI
  Cartographic maps for selected durations and ARI
  Seasonality and Temporal Distributions
  AMS time series data
  Documentation, supplementary information
S. Perica, NOAA/NWS/HDSC Weather Conference, Danbury, 29 September 2018 4
NOAA Atlas 14 products - project area

## Slide 5
Supplementary information
PF graphical
PF tabular
S. Perica, NOAA/NWS/HDSC Weather Conference, Danbury, 29 September 2018 5
NOAA Atlas 14 products – selected location

## Slide 6
Approach: Region-of-influence regional frequency analysis approach based on GEV distribution with parameters calculated based on L-moment statistics from annual maximum series (AMS).
Main steps:
1. Data collection, formatting
2. Examination of geospatial data, station cleanup
3. AMS extraction and quality control
4. Regionalization
5. Calculation of regional moments, distribution fitting
6. Derivation of DDF curves and confidence limits
7. Interpolation (30 arc-sec grid) using PRISM statistical-geographic approach
8. Peer review and revision
9. Development of supplementary products
10. Publication
AMS series
Regionalization
S. Perica, NOAA/NWS/HDSC Weather Conference, Danbury, 29 September 2018 6
NOAA Atlas 14 process
Notes: 6

## Slide 7
Regionalization
Distribution fitting
Interpolation
Smoothing & consistency checks (spatially and across durations and frequencies)
ARI (years) | Potential PF range
100 | 11-13 in
1000 | 13 -22 in
S. Perica, NOAA/NWS/HDSC Weather Conference, Danbury, 29 September 2018 7
Major sources of errors - methods
NA14-TP40

## Slide 8
Record length
n latest years
1hr AMS for ITHACA, NY. Hourly record extended 49 years through digitization; 100-yr estimate changed from 1.6 to 2.5 in.
Spatial coverage
Quality control
Single low outlier reduced 100-year estimate ~35%.
100-yr range: 6.6 – 17 in
100-yr: 3.1 vs 4.8 in
S. Perica, NOAA/NWS/HDSC Weather Conference, Danbury, 29 September 2018 8
Major sources of errors - data

## Slide 9
S. Perica, NOAA/NWS/HDSC Weather Conference, Danbury, 29 September 2018 9
Impact of major storms on estimates
24-hour frequency curves at Houston Hobby Airport.
Percent change in 100-year 24-hour estimates (ver 1) due to Hurricane Harvey.
Tropical storm Charley, 1998
Progression over the years in 24-hour frequency estimates at Del Rio Intl Ap station.

## Slide 10
Record length | # of stations | # of exceedances |  |  | 
 |  | 0 | 1 | 2 | 3
≤ 30 | 129 | 96 | 30 | 2 | 1
31- 50 | 296 | 202 | 78 | 12 | 4
51 - 70 | 356 | 204 | 125 | 25 | 2
71 - 90 | 224 | 104 | 97 | 18 | 5
> 90 | 223 | 89 | 89 | 32 | 13
Record length | # of stations | % of stations exceeding 100 year estimate actual (expected) | 
 |  | 0 times | ≥1 times
≤ 30 | 129 | 74 ( >73) | 26 ( <27)
31- 50 | 296 | 68 (61-73) | 32 (27-39)
51 - 70 | 356 | 57 (49-61) | 43 (39-51)
71 - 90 | 224 | 46 (40-49) | 54 (51-60)
> 90 | 223 | 40 (30-40) | 60 (60-70)
S. Perica, NOAA/NWS/HDSC Weather Conference, Danbury, 29 September 2018 10
Why do 100-year (1000-year) events happen so often?
When talking about the frequency of extreme events, three elements should be specified: duration, location and area size.
Example: analysis of exceedances of NOAA Atlas 14 24-hour 100-year estimates at Texas stations.

## Slide 11
AT-STATION ANALYSIS:
1. Parametric and non-parametric statistical tests for trends in AMS mean and variance
2.Investigate spatial patterns in tests results
Vol 10, 24-hr
positive trend
negative trend
no trend
REGIONAL ANALYSIS:
H0 : no correlation in normalized AMS regressed against time (5% level)
Volume 10 regions
S. Perica, NOAA/NWS/HDSC Weather Conference, Danbury, 29 September 2018 11
Analysis of non-stationary climate in NA14
DATA ANALYZED – AMS:

## Slide 12
METHODOLOGY CHANGE
  In partnership with the Penn State University developed non- stationary NOAA Atlas 14 methodology
  Challenges:
NA14 old | NA14 new | NA14(t) new
15.0 | 19.3 | 20.7
non-stationary
stationary
INCUSION OF (DOWNSCALED) CLIMATE PROJECTIONS DATA
In partnership with the University of Illinois, Urbana-Champaign & University of Wisconsin-Madison
Challenges
  How to develop scientifically defensible methods to incorporate climate projections?
  Can we extract useful information about extreme precipitation at spatial and temporal scales of interest (point, sub-daily)?
S. Perica, NOAA/NWS/HDSC Weather Conference, Danbury, 29 September 2018 12
Non-stationary NA14 - current status, future work